## Slide 1: FPGA Final Project
組員:何文傑、蔡政霖、林言珀
指導教授:陳朝烈 教授

## Slide 2: 軟體工程流程圖
Requirements
Analysis
Design
Coding
Verification

## Slide 3: Annotation
Opcode = 000:
  input A B C  A(128*128)7Bit, B(128*128)7Bit, C(256*256)1Byte
Opcode = 001:
  (0X00,0XFF) – 2D  A*B0 = C
Opcode = 010:
  (0X00,0XFF) --1D  AT B1 = C
Opcode = 011:
  C = A
Opcode = 100:
  Return uart c
Opcode = 101:
  Return VGA c
Opcode = 110:
  nop
Opcode = 111:
  error

## Slide 4: 需求(Requirements) /specifications 規格
1.loop unrolling:同時幾個乘加器(設計array (systolic)的架構)
2.Block RAM 當 FIFO(buffer)存甚麼
3.BRAM control 管理記憶體存放
4.FPGA UART傳遞PC之間的資料溝通
5.VGA顯示照片

## Slide 5: VGA specifications
1. 8 bit Digital to Analogy converter circuit for RGB of VGA
design 8 bit R-2R circuit , output voltage 0 to 0.7 V
2. Horizontal synchronization , vertical synchronization and RGB 8 bit data from FPGA

## Slide 6: UART specifications
1.Baud rate 115200
2.Data 8 bit , Parity none , stop 1 bit
3.Asynchronous receive and transmission data

## Slide 7: BRAM control specifications
1.de Q( Q, Block ram)
2.in Q( Block ram, Q)
3.address counter
  Addr A , increment A
  Addr B , increment B
  Addr C , increment C
4.收config.txt from UART
5.uart 收 A,B,回C blocks

## Slide 8: 分析(Analysis) 架構(Architect)
U
I/O
MAC array
MMU
UART
VGA
Transformer HW RS232
RGB 8bits
DSP48乘加
BRAM control
Result
Src img
FIFO
VHDL
array
BRAM
(Dual port)

## Slide 9: 架構(Architect)
UART
VGA
BRAM
control
BRAM
MAC systolic array
……
……
……
b
a
Only input
Only output

## Slide 10: Design VGA 8 bit R-2R
R = 1 ohm 2R = 2 ohm
RGB Internal resistance

## Slide 11: Design FIFO

## Slide 12: VGA & Block ram unit test
儲存圖片在Block ram 裡，
經由解碼後送往VGA顯示在螢幕上，
螢幕的長寬是800*600。

## Slide 13: Design MAC

## Slide 14: Design MAC unit test block diagram

## Slide 15: Design UART
鮑率產生器
Clock
div
Tx shift buffer
LSB
MSB
Tx buffer
LSB
MSB
TxIF
Tx parity
Dout[7:0]
Tx pin
buffer
Tx pin
Rx pin
buffer
Rx pin
LSB
Rx shift buffer
MSB
Din[7:0]
LSB
Rx buffer
MSB
RxIF
Rx parity
Rx parity
Data Recovery

## Slide 16: Design UART unit test

## Slide 17: Design UART unit test
當PC端按下數字”5”後
轉ASCII碼給FPGA的LED燈顯示0x35
當PC端按下數字”A”後
轉ASCII碼給FPGA的LED燈顯示0x41
UART setup :
baud rate:115200
Data: 8 bit
Parity: none
stop: 1bit

## Slide 18: Design state assignment

## Slide 19
Input A B C

## Slide 20
S00 : 讀opcode, A, B, C size
S01 : 取A, B 的 addr & we
S1 : 解碼  得知使用function 2(2-D)
S2 : 運算  A*B0
2D-array
E1 : 要A, B的 addr & we
E2 : 給指令
E3 : 沒有有效指令
E4 : 進行function 2的運算指令
E5 : 重複運算指令直到運算完成所有數值
E6 : 運算完成

## Slide 21
S00 : 讀opcode, A, B, C size
S01 : 取A, B 的 addr & we
S1 : 解碼  得知使用function 3(1-D)
S2 : 運算  A*B0
1D-array
E1 : 要A, B的 addr & we
E2 : 給指令
E3 : 沒有有效指令
E4 : 進行function 1的運算指令
E5 : 重複運算指令直到運算完成所有數值
E6 : 運算完成

## Slide 22
C = A

## Slide 23
UART FSM

## Slide 24
VGA FSM

## Slide 25
NOP

## Slide 26: 程式(coding) (refinement)

## Slide 27: 除錯(Verification)